###### Rockpanel Woods

A Rockpanel board surface treated with a triple layer water based coating available in a range of 17 standard wood grain finishes.

The surface has excellent UV resistance when tested in accordance with ISO 4893-1&2 and judged in accordance with ISO 105-A02 and ISO 105-A03.

Board dimensions: 3050 x 1200mm

Board thickness: 8 mm

Available in a choice of durable for general applications or Xtreme for applications where greater mechanical strength is required.

Protect plus finish is standard which improves UV protection and provides anti-graffiti and self-cleaning finish.

Rockpanel Woods has been awarded with several ETA certificates.

All Rockpanel standard products have a maximum lead time of 2 weeks.

Please consult Rockpanel BV for advice on use of other Rockpanel Wood’s cladding products in non-ventilated constructions.

(Please delete clauses in red to suit specification)

150 RIGID SHEET CLADDING………….

Product reference:

Rockpanel Woods Durable board

Rockpanel Woods Xtreme board

Material: Inert Rockwool panels with pre-finished decorative coating

Manufacturer: Rockwool Lapinus Productie BV, Industrieweg 15

6045 JG Roermond, The Netherlands

Sales Representative: Rockwool Rockpanel BV, Wern Tarw, Pencoed, Bridgend CF35 6NY.

Tel: 01656 863210.  Fax: 01656 863611.

E-Mail: info@rockpanel.co.uk.  Web: www.rockpanel.co.uk.

Thickness: 8mm

Finish: Protect Plus as standard

Colours:

Cherry / Teak / Oak / Maple / Mahogany / Beech / Alder / Merbau / Rhinestone Oak / Ceramic Oak / Marble Oak / Slate Oak / Carbon Oak /

Ebony Slate / Ebony Granite / Ebony Marble / Ebony Limestone

Fixings:

For Aluminium:

# Aluminium (AlMg5)Rivet with colour match head minimum Ø 14mm, length 18 mm and shank diameter 5 mm.	Pre-drill Rockpanel with 9mm holes and 5.5mm for centre fixings.  A spacer tool should be used when fixing rivets.

# Ref: RP/fix 20 Stainless steel (A4 grade) self tapping screws (thickness aluminium between 1,2 and 2,5 mm) with colour matched heads. Please note when using self tappers the maximum panel size is 1500 x 1200mm.

# For Steel:

# Ref: RP/fix 20 Stainless steel (A4 grade) self tapping screws with colour matched heads.

Ref:	River/spacer tool

Number and location:

Rivets and self-tappers to be fixed at a maximum span of 600 mm and maximum 600 mm vertical centres.

Please consult Rockpanel BV for wind loading calculations

Fixings to be positioned minimum 15mm from the vertical edge of the board and minimum 50mm from the horizontal edge of the board.

Joints

Type/treatment:

Vertical joint treatment:

If desired, blackout tape can be applied to prevent light reflection from aluminium supports.

### Horizontal joint treatment

Rockpanel profile A: Aluminium horizontal chair section (with high back)

Rockpanel profile B: Aluminium horizontal V-bird section

### External Corner Treatment

8mm boards

Rockpanel profile D: External corner profile (aluminium)

Rockpanel profile E: External capped corner profile (aluminium)

Colour: Colour matched to board/Black/White

Distance between boards: Minimum of 6mm

Air gap:  Minimum 25mm –

Consult Rockpanel for recommendations and details if designing to NHBC requirements

In accordance with ETA Approval for example:

Secondary support system/framing system;

Product reference:	Plastestrip Top Hat and Z profile system

Material:	Aluminium

26mm cavity

Ref: AL/TH/26/50 - Top Hat Profile

Ref:AL/Z/26/50/26 - Z profile

40mm cavity

Ref: AL/TH/40/55 - Top Hat Profile

Ref:AL/Z/40/55/26 - Z profile

#### Fixings: number and location

Consult with Plastestrip for recommendations and details

For cavities greater than 40mm – 270mm contact Plastestrip for further details

Thermal Insulation: As clause H92 775

Breather membrane:	As clause H92 785

Rockpanel Accessories:

### Bottom Drips

Rockpanel profile J: aluminium bottom drip profile

General Accessories:

Ventilated profiles:

Ref: 025/10K	bottom vent strip – 25mm cavity

Ref: 065/10K	bottom vent strip – from 30-65mm cavities

Ref: 090/25K	bottom vent strip – from 65-90mm cavities

Ref: 125/25K	bottom vent strip – from 90-125mm cavities

Manufacturer: Plastestrip (Profiles) Ltd, 1 Enterprise Park, St Austell, Cornwall, PL25 4EJ.

Tel: 01726 74771. Fax: 01726 69238.

E-Mail: sales@plastestrip.com Web: www.plastestrip.com

# GENERAL REQUIREMENTS

- CONTROL SAMPLES

- General: Complete an area of the cladding and obtain

approval of appearance before proceeding.

  - Location :……….

  - Extent of area……….

- FIXING SHEETS

- General: Secure to supports without producing distortion.

- Fasteners: Evenly spaced in straight lines, in pairs across

joints and sufficient distance from edge of sheet to prevent

damage.

- COVER STRIPS

- General: Form straight runs in single lengths wherever possible

- Location and method of forming joints: Submit proposals where

not detailed.