# H20 RIGID SHEET CLADDING

155 SHEET CLADDING………….

Rockwool Rockpanel products are formed from compressed Rockwool with thermo-hardening synthetic binding compounds to produce a “dimensionally stable” and inert panel. Rockpanel products are not affected by moisture or thermal changes. Normally the construction requires ventilation and water drainage. When designing the system ensure only vertical battens are used, there is provision for water escape and flashing details are taken into consideration.

Rockpanel products are water repellent and inherently “fire-safe” and will not propagate the fire. They are classified as class “O” as defined in the Building Regulations and achieve at least class B-s2, d0 (FS-Xtra boards A2-s1, d0) according the EU fire classes.

Rockpanel products maybe cut on site with normal working tools, for large areas Rockpanel BV recommend the use of a table saw or circular saw using a 64 tooth TCT fine cut blade.

Rockpanel products can be fixed in ventilated constructions. Rockpanel Rockclad and Rockpanel Structures can in some situations applied in a non ventilated application. For use of non ventilated applications as also consequences by other Rockpanel products, please contact Rockpanel BV for advice.

# Ventilated back drained cladding systems

Rockwool Rockpanel BV produces 8 cladding products suitable for rigid sheet cladding.

## Rockpanel Rockclad

##### Rockpanel Structure

###### Rockpanel Woods

Rockpanel Metallic

Rockpanel Chameleon

Rockpanel Natural

Rockpanel Lines II S & L